## Slide 1: “Count the Duplos on the table.”
Josh Villbrandt
28 Nov. 2011
CSCI 547
Keywords: ROS, PCL, Kinect

## Slide 2: Algorithm Reasoning
To count Duplos, they must first be identified
  Strong attributes include color and shape
Color trainer
  Segments the block from background, finds mean color and standard deviation
Shape trainer
  Segments the block from background and a glove (knowing glove color)
  Continuously adds subsequent clouds together using VHF descriptors
  On save, align block to axes using two biggest planes -> orientation
To identify
  Segment from background, then by color, than by distance
  Touching blocks of same color are currently return with unidentified shape

## Slide 3: Implementation Details
Programs
  Created “identify_duplos” package in ROS
  Includes “trainer”, “identify”, “visualize”
Colors Recognized
  Trained on solid red, orange, yellow, dark green, dark blue
Shapes Recognized
  Trained on standard 2x2, 2x4, 2x6, 2x8 blocks
Performance
  Full pose estimate runs as slow as 0.1 Hz on home computer, single thread
  Quick mode operates at ~2 Hz on the same data set, single thread
    bad orientation, position not at centroid, shape based on number of points

## Slide 4: “Training”
remove surface
narrow FOV
filter out glove
statistical noise removal
Fast Point Feature Histograms for target and template
align via Sample Consensus Initial Alignment
transform template
set target to sum of target and transformed template

## Slide 5: “Training” Examples
(left) Kinect viewing 2x2 Duplo
(right) isolated Duplo shown in rviz

## Slide 6: “Identify”
color: color with least error from average
shape: size of particle filter (conditioned on voxel grid)
position: average position of all particles
orientation: normal vector of largest plane in block cluster
color: color with least error from average
shape: result of best aligned template
position: given as centroid of template
orientation: given as normal vector of template
Quick Mode
Template Align Mode

## Slide 7: “Identify” Examples
(left) config file, built from training
(right) ROS message, shown w/ rostopic

## Slide 8: “Visualize” Examples
(left) Kinect at home (quick mode)
(right) group2_3.pcd/PR2 (quick mode)

## Slide 9: Steps for Improvement, Further Development
Better shape building / pose estimation (FPFH alone limited to three faces)
  Possibly limit rotation during SAC alignment search for continuous build
HSV color to remove dependence on brightness
Drop-in OpenMP replacements for PCL functions
Try separating touching blocks of same color by applying and removing known shapes
Internal Bayes filter could handle occlusions ^_^
  From robot arm
  So many blocks, one gets covered
  Rotation